## Slide 1: Efuse User Guide
2018.01.22

## Slide 2: Cli install setup in Amlogic Platform
檢查 wifi interface 是否正常
  需確認開機前先全完斷電，否則可能造成下次USB interface無法重新認卡，可能會造成wifi interface無法帶起
第一次使用adb 時，需讓amlogic platform去信任NB/PC主機(透過GUI)
如果利用USB port來進行adb command，USB port type 需為 OTG
-請參閱Pag 3 & Page4
Non-adb 時的cli install setup
-請參閱Pag 5
在進行RF tool前，需確認無wireless連線,並確認硬體架構設定
-請參閱Pag 6 & Page 7

## Slide 3: adb install & adb command
Install adb command (如果電腦上沒有adb-tool就必須安裝)
  http://bernaerts.dyndns.org/linux/74-ubuntu/328-ubuntu-trusty-android-adb-fastboot-qtadb
  備註:adbUbuntu 14.04 - Install Android Tools
Amlogic platform adb command
  adb root
  adb remount
  adb shell

## Slide 4: cli install (adb)
Push cli to device(Amlogic)
  adb push cli /system/bin/cli(更改執行權)
Change cli mode
  adb shell
  chmod 777 /system/bin/cli

## Slide 5: cli install (non-adb)
Console command
  mkdir /data/temp
  mount –o rw,remount /system
    [change filesystem /system to read/write]
  mount –t vfat /dev/block/sda1 /data/temp
    [mount usb storage to /data/temp]
  cp /data/temp/cli /system/bin/cli
  chmod 777 /system/bin/cli
  umount /data/temp

## Slide 6: Hardware Setup
SSV6266P
GND/RX/TX
UART
amlogic platform S905
HDMI
  25MHz晶振
OTG Port
Ant端

## Slide 7: Hardware Setup
在進行RF tool前，需確認無wireless連線
如果利用USB port來進行adb command，USB port type 需為 OTG
amlogic platform S905
Non-adb時須利用UART來操作

## Slide 8: Efuse command
cli efuse [r|w] [category] [value]
  cli efuse r freq
    Read xtal frequency offset from efuse
  cli efuse r txpower1
    Read txpower1 from efuse
  cli efuse r txpower2
    Read txpower2 from efuse
  cli efuse r mac
    Read mac address from efuse
  cli efuse r ht40rate
    Read ht40rate from efuse

## Slide 9: Efuse command
cli efuse [r|w] [category] [value]
  cli efuse w freq [value]
    write xtal frequency offset to efuse
  cli efuse w txpower1 [value]
    write txpower1 to efuse
  cli efuse w txpower2 [value]
    write txpower2 to efuse
  cli efuse w mac [value]
    write mac address to efuse
  cli efuse w ht40rate
    write ht40rate to efuse